## Slide 1: Airworthiness directives at Anfa
New mechanics, first month
Quality: Karim Bennani
Notes: This deck is for mechanics in their first month. It covers how we decide whether a directive applies and how we record it. Ask the quality manager about anything it does not cover.

## Slide 2: Where directives come from
The state of design issues them: the FAA for our Cessnas
Published in the Federal Register
Revisions and corrections follow
Notes: Corrections are published as separate notices, sometimes weeks later. A correction can change the applicability or a compliance time. AD 2020-16-08 on the Aspen displays is an example: read the rule and its correction together.

## Slide 3: Check applicability before you sign
Model and serial number range
Installed equipment and part number
Software version, modifications
Notes: Two traps in our own fleet. CN-TFC is a 172S like CN-TFA and CN-TFB, but its serial number is above the range of AD 2013-11-11. CN-TFD has a KAP 140 autopilot, but its serial number is outside the range of the KAP 140 directives. Equipment alone is not enough, and serial numbers alone are not enough.

## Slide 4: The engine oil pressure switch
P/N 83278, 3,000 hours
Replace with a new, zero-time switch
Record part number, date, and airframe hours
Notes: The 50-hour allowance in paragraph (g)(6) of AD 2013-11-11 applied once, to switches that were already at or near the limit when the directive took effect on 1 August 2013. It is not a grace period you can use today. Our manual, section 3.2, applies the same 3,000-hour limit to every 172R and 172S we maintain.

## Slide 5: Torque
Maintenance manual first
AC 43.13-1B Table 7-1 when it gives no value
Record the wrench number
Notes: Read the notes printed with Table 7-1 before you use it: they limit when its values apply. If a value looks wrong, stop and ask; do not guess between two columns.

## Slide 6: Records
14 CFR 43.9 content in every entry
AD compliance record for each aircraft
Hours to one decimal place
Notes: Check every number you copy. A swapped pair of digits in an installation time moves the next due time by 90 hours, and nobody notices until the records are audited.